## Slide 1: 9Megapixel 360-degree Camera for SE ver.2.00 Model: WV-X4171/X4170 (Indoor) WV-X4571L/X4571LM (Outdoor Vandal)
23rd Feb. 2018
Panasonic Corporation
Notes: 摂氏→華氏 F=(9/5)*C + 32 華氏→摂氏 C=(5/9)*(F-32)

## Slide 2: Welcome & Disclaimer
2
This document, Ver. 2.00, is updated from previous Ver.1.00.
Hence some of the specification & function detail might be changed without announcement.
This document is not cover all over about the product. Therefore, please utilize this document together with other materials such as “Installation Guide”, “Operating Instructions”, “Quick Reference Guide” “Specification Sheet” and “Product Presentation Material” so on as necessary.
These materials can be downloaded from the following website.
http://security.panasonic.com/download/

## Slide 3: Version History
No | Update contents | Page No. | Version | Editor | Update
- | 1st Version |  | Ver.1.00 | A. Yamani | 9.Feb.2018
1 | Add typical GUI image | 64-81 | Ver.2.00 | A. Yamani | 23.Feb.2018
3
Notes: 288kmph= カトリーナ：280 km/h
伊勢湾台風=270km/h

## Slide 4: Contents
Concept
Key features
      Extreme Visibility
      Extreme Compression
Image Capture mode
Supported Resolution
System Configuration
Specification Comparison
Bundled Items and Options
Model Number
Appearance
4
      Extreme Data Security
      Extreme Simplicity
      Other Features

## Slide 5: Product Concept
5
WV-X4171/X4571L will be launched as a successor to WV-SFN480/SFV481.
WV-SFN480
WV-SFV481
WV-X4171/X4170
WV-X4571L/X4571LM
H.264
H.265
Existing 9M 360-deg. camera
New 9M 360-deg. camera
New Line-up of i-PRO Extreme series camera
Support H.265 codec
X4170
X4571LM
X4171
X4571L

## Slide 6: Product Concept
Solution
Enables to reduce bitrate by H.265 codec and new Smart Coding feature, “Frame rate control”
Reduce data size with the same image quality
FIPS140-2 (Industry first)
Cost saving for certificate
Covering Wide Variety Reduce
and Number of Cameras
Long term recording
NW stress reduction
EXTREME
Visibility
EXTREME Compression
EXTREME
Data Security
EXTREME
Simplicity
People counting, Heat-map and MOR
New People counting
Support Intelligent Functions * Required Optional License
Provide High secure system by Symantec certificate
Protect Image Data from the hacking
Improve Monitoring Efficiency
Face recognition distance: 6m
Super Dynamic range: 108dB
Coverage in the Night: 10m
Face visibility of a moving person: No.1 in industry
Industry's best peripheral resolution and compression performance
Needs
Focus Point
Appeal Point
Good peripheral resolution by stereo projection lens
Improved Wide dynamic Range by 108dB (SFN480/SFV481: 84dB)
Built in IR-LED : Max. 10m Reach distance (only WV-X4571L)
Provide best image by “Intelligent Auto (iA)”
Support Various dewarp mode (as same as Current 9M360 deg. Camera)
6
X4170
X4571LM
X4171
X4571L

## Slide 7: Key Features
7
Extreme Visibility
  Peripheral Resolution by Stereo projection lens
  Super Dynamic 108dB
  Built in IR-LED supports 10m (only WV-X4571L)
  iA (intelligent Auto)
  Support Various dewarp mode (as same as current 9M 360 deg. Camera)
Extreme Compression
  H.265 + Smart Coding
Extreme Data Security
  Secure communication by Symantec certificate
  FIPS 140-2 Level 1 compliant
Extreme Analytics
  New People Counting * ASE303W
  People Counting, Heat-map and MOR * SAE200
WV-X4171/X4170
(Indoor)
WV-X4571L/X4171LM
(Outdoor Vandal with IR-LED)
Other Features
  IP66, IK10 support *WV-X4571L (Vandal Resistant Outdoor model)
  Anti-corrosion screw
  SD card error display
  Built in Dehumidifier
New 9M 360-deg. camera

## Slide 8: Key Features
8
8
Extreme Visibility
  Peripheral Resolution by Stereo projection lens
  Super Dynamic 108dB
  Built in IR-LED supports 10m (only WV-X4571L)
  iA (intelligent Auto)
  Support Various dewarp mode (as same as current 9M 360 deg. Camera)
Extreme Compression
  H.265 + Smart Coding
Extreme Data Security
  Secure communication by Symantec certificate
  FIPS 140-2 Level 1 compliant
Extreme Analytics
  New People Counting * ASE303W
  People Counting, Heat-map and MOR * SAE200
Other Features
  IP66, IK10 support *WV-X4571L (Vandal Resistant Outdoor model)
  Anti-corrosion screw
  SD card error display
  Built in Dehumidifier
New 9M 360-deg. camera
WV-X4171/X4170
(Indoor)
WV-X4571L/X4171LM
(Outdoor Vandal with IR-LED)

## Slide 9: Peripheral Resolution by Stereo projection lens
Projection Type | Peripheral resolution / image | Formula (y: image height)
Stereographic | High resolution / Low distortion | 
Orthogonal | Low resolution / High distortion | 
WV-X4171 (New 9MP)
Extreme
Visibility
Panasonic fisheye camera applies stereo projection lens, it enable higher resolution and lower distortion image around peripheral than normal lens.
9m
* Camera height: 3.0m
* Illuminance: Approx. 800lx
θ
A
A’
y
f
lens
sensor
Low Peripheral resolution and high distortion
Stereographic
Orthogonal
High Peripheral resolution and low distortion
X4170
X4571LM
X4171
X4571L
9

## Slide 10: Image Comparison: Resolution of peripheral part
Extreme
Visibility
New camera can provide clear face image even 9m ahead.
10
WV-X4171 (New 9MP)
WV-SFN480 (Existing 9MP)
* Camera height: 3.0m
* Illuminance: Approx. 800lx
X4170
X4571LM
X4171
X4571L
9m
9m
6m
9m
9m
6m

## Slide 11: Image Comparison: Resolution of peripheral part
Extreme
Visibility
Comparison with 5M 360-deg. camera
11
WV-X4171 (New 9MP)
WV-S4150 (5M 360-deg. camera)
* Camera height: 3.0m
* Illuminance: Approx. 800lx
X4170
X4571LM
6m
6m
6m
9m
9m
6m

## Slide 12: Image Comparison: Low Illuminance
Extreme
Visibility
Min. Illuminance specification is 0.3lx same as existing 9M.
12
WV-SFN480 (Existing model)
Min. Illuminance Specification: 0.3lx
WV-X4171 (New 9MP)
Min. Illuminance Specification: 0.3lx
* Shooting environment: 0.5lx
X4170
X4571LM
X4171
X4571L

## Slide 13: Image Comparison: Super Dynamic
Extreme
Visibility
13
Implement Super Dynamic: 108 dB
WV-SFN480 (Existing model)
WV-X4171 (New 9MP)
X4170
X4571LM
X4171
X4571L
Dynamic range: 84db (Reference)
Outside the window white jump
Dynamic range: 108db
Visible outside the window

## Slide 14: Image Comparison: iA (Intelligent Auto)
Extreme
Visibility
14
14
Automatically adjusts to the optimum image quality parameter according to the shooting scene
WV-SFN480 (Existing 9MP)
* Shooting environment: Approx. 800lx
WV-X4171 (New 9MP)
X4170
X4571LM
X4171
X4571L

## Slide 15: iA (Intelligent Auto)
15
Intelligent Auto
Automatically optimizes camera parameters for best tuned image for various scenes, using techniques like Full Auto Shutter & Iris control, Backlit compensation , auto image stabilization.
It also can detect characteristics and movement within the scene to optimize camera settings to provide best fit picture quality.
ON
ON
OFF
OFF
Extreme
Visibility
X4170
X4571LM
X4171
X4571L
Notes: Innovative Visibility
Automatically detect scenes and optimize parameter settings
to enable clear shot of the face and license plate number.
Backlit Scene
Moving Object
Show clearly by shortening the shutter speed of only moving thing.
License plate in the low light
Low light SD performance went up.

## Slide 16: iA (intelligent Auto)
iA enables “sharper, less blur” image of moving object and “higher contrast“ facial image by changing “shutter speed” and “contrast” than normal (means iA “OFF”) mode.
iA applies stronger image effect than normal mode according to shooting object. So iA doesn’t have fixed parameter.
iA has two sub parameter, “motion priority” and “face priority”. You may change parameter but firstly, SSBD recommends to use as iA “ON” without changing any priority and to change only if they want to emphasize efficiency. Please see guideline of next slide and please understand side effect also appears if you change priority.
Since setting of SD (super dynamic) depends on suitable scene or favorite of customer, SD setting is separated from iA menu. User enables to select on or off. Even if SD is off, iA control BLC or HLC to increase contrast of face. However SSBD recommends to use SD on.
Effect of “Motion iA” is limited in case of fixed shutter mode or flicker less mode. It recommends to use as outdoor scene mode.
16
Extreme
Visibility
X4170
X4571LM
X4171
X4571L

## Slide 17: iA (intelligent Auto): Setting Guide Line
Set “iA” as Default Parameter
Image is still blur
Countermeasure | Increase Motion priority level and check result
Effect | Value 0 : Same as normal mode Value 128: Max. 8 times faster shutter speed Value 255: Faster shutter speed than mid value
Side effect | If too fast shutter speed, S/N ratio of image becomes worse because AGC increase gain of noise. If gain level is controlled at low, image becomes dark.
17
Extreme
Visibility
Note: “Face priority” is not applied 9MP 360 deg. camera
X4170
X4571LM
X4171
X4571L
Notes: Innovative Visibility
Automatically detect scenes and optimize parameter settings
to enable clear shot of the face and license plate number.
Backlit Scene
Moving Object
Show clearly by shortening the shutter speed of only moving thing.
License plate in the low light
Low light SD performance went up.

## Slide 18
Intelligent Function in the Night
IR_OFF
IR_ON
Intelligent functions are available.
Intelligent functions are not available.
Maximum detection distance =10m
- IR LED light intensity : High
- Peripheral intensity control : On
Intelligent functions will not effectively work in the following situations or may sometimes be malfunctioning.
• There is no difference in luminance level between the moving object and background.
• Outside light (sunlight, headlights, etc.) enters the shooting area.
• Fluorescent light is flickering.
• Weather condition is extremely poor.
• The detection area is blocked with shadows.
Note
X4571LM
X4571L
When using IR-LED, the intelligence function can be used if it is within the range of 10m
18
Extreme
Visibility
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 19: Various Image Processing
Support various De-warp mode by camera (as same as SFN480/SFV481)
19
Extreme
Visibility
1. Double Panorama
Displayed with distortion correction performed on a 180° image for half of a fisheye image. (2560x1440 to 320x180 selectable)
Stream (1)
Stream (2)
2. Panorama
Displayed with distortion correction performed on the 180° horizontal angle view part of the center of a fisheye image. (2560x1440 to 320x180 selectable)
3. Fisheye
Displayed without performing distortion correction as a fisheye image. (2992x2992 to 320x180 selectable)
4. Single PTZ
Display one specified area with electronic PTZ. Position of area to be displayed can be specified. (2560x1920~QVGA selectable)
5. Quad PTZ
Display the specified 4 areas with electronic PTZ. Position of 4 areas to be displayed can be specified. Distributed as 2 x 2 divided 1 image. (2560x1920～QVGA selectable)
6. Quad Stream
Distribute each channel of 4 PTZ separately (1280 x 960 ~ QVGA selectable) It is possible to simultaneously deliver 4 images PTZ.
X4170
X4571LM
X4171
X4571L

## Slide 20: Key Features
20
Extreme Visibility
  Peripheral Resolution by Stereo projection lens
  Super Dynamic 108dB
  Built in IR-LED supports 10m (only WV-X4571L)
  iA (intelligent Auto)
  Support Various dewarp mode (as same as current 9M 360 deg. Camera)
Extreme Compression
  H.265 + Smart Coding
Extreme Data Security
  Secure communication by Symantec certificate
  FIPS 140-2 Level 1 compliant
Extreme Analytics
  New People Counting * ASE303W
  People Counting, Heat-map and MOR * SAE200
Other Features
  IP66, IK10 support *WV-X4571L (Vandal Resistant Outdoor model)
  Anti-corrosion screw
  SD card error display
  Built in Dehumidifier
New 9M 360-deg. camera
WV-X4171/X4170
(Indoor)
WV-X4571L/X4171LM
(Outdoor Vandal with IR-LED)

## Slide 21: Extreme Compression: H.265 HEVC
H.265 is next generation of video codec. After standardize, it’s now ready to apply
The 1st version of the HEVC standard was finalized in April 2013.
The 2nd version of HEVC including the RExt, SHVC and MV-HEVC extensions was finalized in October 2014.
The 3rd version of HEVC including the 3D-HEVC extension was finalized in February 2015.
2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
HEVC ver.1 Standard
April
HEVC Profile Extension
OCT
HEVC SVC Extension
HEVC 3D Extension
Feb
HEVC MV Extension
HEVC SCC Extension
Feb
Format Range Extension (RExt)
Scalability Extension (SHVC)
3D Extension(3D-HEVC)
Multiview Extension(MV-HEVC)
Screen Content Coding Extension(SCC)
- Main Profile (4:2:0 8bit)
→ Equivalent to
H.264 Main/High Profile
- Main10 Profile (4:2:0 10bit)
→ 4:2:0 10bit
- Main Still Profile
21
Extreme
Compression
X4170
X4571LM
X4171
X4571L

## Slide 22: Extreme Compression: H.265 HEVC
H.265 improve encoding efficiency more than H.264. It reduces bitrate by 50% compared H.264 (legacy and other competitor) and 30% compared Panasonic latest H.264 camera.
1.36/1.93≒70%
(30% reduced)
RD curve (relation with image quality and bitrate)
 | H.264/AVC | H.265/HEVC | 効果
Coding tree unit | 16x16 | 8x8, 16x16, 32x32, 64x64 | High efficiency of Encoding
prediction blocks | 4x4–16x16 unit | 4x4-64x64 unit | 
Transform | 4x4, 8x8 DCT | 4x4-32x32 DCT, 4x4 DST | 
Quantization | 4x4, 8x8 quantization matrix | 4x4-32x32 quantization matrix | 
Intra-prediction | 8direction + DC | 33direction + DC + Planer | High accuracy of prediction
inter-picture prediction | -interpolation with an 6-tap filter -motion vector prediction (one candidate) | -interpolation with an 8-tap filter -motion vector prediction (many candidate) | 
Loop filters | De-blocking filter | De-blocking filter Sample Adaptive Offset(SAO) | Decoded image quality improvement
Entropy coding | CABAC CAVLC | CABAC | High efficiency of Encoding
HEVC apply large prediction block for plane area. This educes number of block and save total data size
RD curve is one of the subjective evaluation method of image quality.
According to encoding test by using official video clip, we can save 30%. (Generally 50%)
Panasonic H.265
Panasonic H.264 (latest codec)
22
Extreme
Compression
X4170
X4571LM
X4171
X4571L

## Slide 23: Smart Coding
23
Extreme
Compression
Smart coding Technology | WV-S4150/S4550L
Encoding load Reduction | GOP control Apply long term P frame in advanced mode: I-Frame interval is fixed every 60sec but long term P frame which enables to create image with only previous I-frame is inserted every 1 sec.
 | Frame rate control （NEW） Control the frame rate with / without motion, it is the installation value in the case of motion, and in the case of no motion it drops from the set value Available Transmission Priority: VBR mode only
 | AUTO VIQS Improved image quality by low pass filter
Support Transmission mode | GOP : Low / Mid / Advanced mode: VBR : Advanced mode: Constant bit rate, Frame rate and Best Effort AUTO VIQS : all transmission type
Support Stream | Stream 1-2 1st stream: GOP and AUTO VIQS 2nd stream: GOP only
X4170
X4571LM
X4171
X4571L
WV-X4171/X4571L camera enhances smart coding technology by applying “New Control Mode”.

## Slide 24: Smart Coding – Frame Rate Control (New)
24
Frame rate control
Extreme
Compression
GOP type | Motion | No motion
I-frame interval | 4s | 16s to (FPS* 16) s (increase gradually) (16s to 480s @ 30fps)
Number of frames of GOP | FPS * 4 (120@30fps) | FPS * 16 (480 @30fps)
Frame Rate | Keep frame rate setting | Reduced frame rate and reach 1fps
GOP @No motion
P P P
P P P
i-frame
480 frames@30fps
GOP @Motion
P P P
i-frame
120 frames@30fps
15fps
7.5fps
3fps
1fps
30fps
No motion
Different type of GOP is applied at motion and no motion.
If there is no motion, camera reduces frame rate gradually and finally it reaches 1fps. This means max. i-frame interval becomes 480sec.
No Motion
1sec
1/3sec
Extend time scale
With keeping same number of frame
Extend GOP
Like bellows
0s
16s
48s
112s
272s
752s
Motion
16s
32s
64s
160s
480s
30fps
X4170
X4571LM
X4171
X4571L

## Slide 25: Smart Coding – Frame Rate Control (New)
25
Frame rate control
By dynamically controlling the frame rate in addition to the refresh interval depending on the presence or absence of motion, the bit rate at the time of scene shooting without motion is further reduced.
(Example: In case of Frame rate = 30fps)
30fps
16s
15fps
32s
7.5fps
64s
3fps
160s
1fps
480s
i-frame
i-frame
P P P
・ ・
P P P
P P P
・ ・ ・ ・ ・ ・ ・ ・
P P P
P P P
P P P
P P P
・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・
P P P
・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・
・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・
P P P
P P P
i-frame
i-frame
i-frame
i-frame
Without Motion
Without Motion
With Motion
Extreme
Compression
Depending on the situation, the frame rate drops.
It will drop to 1 fps as maximum.
When 1 fps, the I frame interval becomes 480s.
The frame rate and I frame interval will be changed as a set, such as 30fps/16s, 15fps/32s, 7.5fps/64s, 3fps/160s and 1fps/480s.
Pattern 1: Without Motion all the time
Pattern 2: Motion restoration
Motion detected
When motion is detected, frame rate will be increased up to 30fos (In case of Frame rate = 30 fps)
I frame interval will be changed between 4s and 16s depend on the situation whether there is motion.
When there is no more motion again, the operation of above Pattern 1 is repeated.
1fps
480s
1fps
P P P
P P P
P P P
・ ・ ・ ・ ・ ・ ・
P P P
・ ・
・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・
P P P
P P P
i-frame
i-frame
i-frame
i-frame
30fps
4s
・ ・
P P P
P P P
30fps
4s
Without Motion
No Motion again
30fps
16s
15fps
32s
i-frame
i-frame
P P P
・ ・
P P P
P P P
・ ・ ・ ・ ・ ・ ・ ・
P P P
X4170
X4571LM
X4171
X4571L

## Slide 26: Smart coding
26
Extreme
Compression
 | GOP control |  | Auto-VIQS | Smart Facial Coding
H.264 Mode | OFF | - | - | 
 | Low | I frame interval: 1 sec to 8 sec | - | N/A
 | Mid | I frame interval: 4 sec to 16 sec | - | N/A
H.265 Mode | OFF | - | - | 
 | Low | I frame interval: 1 sec to 8 sec | OFF | N/A
 |  |  | ON | N/A
 | Mid | I frame interval: 4 sec to 16 sec | OFF | N/A
 |  |  | ON | N/A
 | Advanced | I frame interval: 60 sec | OFF | N/A
 |  |  | ON | N/A
 | Frame rate control | I frame interval / Frame rate Motion : 4 sec No Motion：16sec/[FPS] ~ [FPS*16]sec/1fps (@30fps, 16sec/30fps ~ 480sec/1fps) | OFF | N/A
 |  |  | ON | N/A
X4170
X4571LM
X4171
X4571L
Frame rate control mode is newly added same as 5M 360-deg. Camera.
Smart Facial coding is not supported.

## Slide 27: Extreme Compression : Smart coding (H.265 mode)
27
X4170
X4571LM
X4171
X4571L
Below is one of the reference “Sample measured” result of smart coding.
Result may change on actual environment, light condition and frequency of motion.
Scene | Smart Coding | I frame interval | Auto-VIQS | Bitrate (kbps)
No motion | OFF | 1sec | OFF | 4198
 | MID | 16sec | OFF | 1052
 |  |  | ON | 224
 | Advanced | 60sec | OFF | 335
 |  |  | ON | 295
 | Frame Rate Control | 480sec with 1fps | OFF | 19
 |  |  | ON | 8
Scene | Smart Coding | I frame interval | Auto-VIQS | Bitrate (kbps)
With Motion | OFF | 1sec | OFF | 8120
 | MID | 4sec (to 16sec) | OFF | 5344
 |  |  | ON | 737
 | Advanced | 60sec | OFF | 956
 |  |  | ON | 387
 | Frame Rate Control | 4sec with 30fps | Same as “MID” with motion | 
Extreme
Compression

## Slide 28: Key Features
28
Extreme Visibility
  Peripheral Resolution by Stereo projection lens
  Super Dynamic 108dB
  Built in IR-LED supports 10m (only WV-X4571L)
  iA (intelligent Auto)
  Support Various dewarp mode (as same as current 9M 360 deg. Camera)
Extreme Compression
  H.265 + Smart Coding
Extreme Data Security
  Secure communication by Symantec certificate
  FIPS 140-2 Level 1 compliant
Extreme Analytics
  New People Counting * ASE303W
  People Counting, Heat-map and MOR * SAE200
Other Features
  IP66, IK10 support *WV-X4571L (Vandal Resistant Outdoor model)
  Anti-corrosion screw
  SD card error display
  Built in Dehumidifier
New 9M 360-deg. camera
WV-X4171/X4170
(Indoor)
WV-X4571L/X4171LM
(Outdoor Vandal with IR-LED)

## Slide 29: Secure Communication
29
 | Symantec certification | AES 256bit Encryption | Secret Sharing Scheme | Supported devices |  | 
 |  |  |  | i-PRO System | VI | Other VMS
SSL communication |  |  |  |  (between camera, NX series NVR and ASM300) |  |  *limited
Data encryption | - |  |  |  (SD card recording) (between camera and NX series NVR) (between camera and ASM300 *NX series NVR is necessary) (between NX series NVR and ASM300) | N/A | N/A
Device certificate (*Future function) |  | - | - |  (only between camera and NX series NVR) | N/A | N/A
Alteration Detection |  | - | - |  (with tool) | N/A | N/A
Pre-installed certification by Symantec and latest technology for SSL & data encryption realize
“highly secured communication system”
Pre-installed certification of Symantec realizes high reliability for SSL communication and high secured device certification*
Encryption module of SSL meets FIPS 140-2 Level1 (CAVP), which is U.S. government computer security standard
Encryption of SSL and data encryption support latest “AES-256bit key” strong encryption (usually used 128bit long key)
Continuous Vulnerability Test contributes to find latest security risk and take measure against risk quickly
Panasonic applies secret sharing scheme to save resources of data encryption
When using secure communication function with NX series NVR, optional license will be required.
* Detailed information are explained in Secure material for SE
Extreme
Data Security
X4170
X4571LM
X4171
X4571L

## Slide 30: Secure Communication: Data encryption
30
Generally, data encryption requires a lot of memory and CPU resources for encryption and decryption.
By applying “Secret Sharing Scheme” before encryption,
Panasonic enables to reduce the amount of encrypted data and save resource.
■H.264 (1Frame)
Secret Sharing Technology
AUD
SPS
PPS
SEI
SEI
Picture Data
NAL
■Encrypted H.264 (1Frame)
AUD
SPS
PPS
SEI
SEI
AES
NAL
Sharing Data
Sharing Data
Sharing Data ⑨
9 : 1
Data encryption by AES 256bit key
Secret sharing scheme is to separate secret data into parts and keep those parts separately to enhance security of saving data.
Data is possible to restore only if all parts are collected. Even one missing part disables to restore original data.
By using this scheme, Panasonic encrypts only one part of data and contribute to reduce device resources.
Note: “Data encryption” will be supported from next version up
* Detailed information are explained in Secure material for SE
Extreme
Data Security
X4170
X4571LM
X4171
X4571L

## Slide 31: Secure Communication
31
Why Symantec?
Symantec certification is pre-installed into hardware of i-PRO cameras at factory.
  No need to install certification manually
  Someone doesn’t able to re-write and remove certification
Symantec issues reliable certification for i-PRO cameras
  It is certified by reliable organization “Symantec”
  Much more reliable than self-certification as competitor
Why Panasonic SSL is reliable?
There are a lot of vulnerability report related to Open SSL,
on the other hand, Panasonic has in-house encryption module.
Extreme
Data Security
* Detailed information are explained in Secure material for SE
X4170
X4571LM
X4171
X4571L

## Slide 32: Camera Limitation of SSL and Data encryption
32
Max total camera bandwidth will be reduced to 16Mbps from 50Mbps , when you use SSL or Data encryption function, because a lot of processing load is required.
Actually bandwidth of stream with SSL is approx. 0.4% larger than normal stream.
Bandwidth of stream with Data encryption is as same as normal stream.
SSL supports stream(1 )-(4) of H.265/H.264 and JPEG(1)-(3). However, you can not turn “On/Off” SSL each stream separately.
Data encryption supports only stream(1), stream(2) of H.265/H.264 and JPEG(1)- (3). Support AAC codec. (G.711 and G.726 are not supported)
You can turn “On/Off” Data encryption each stream separately.
Extreme
Data Security
* Detailed information are explained in Secure material for SE
X4170
X4571LM
X4171
X4571L

## Slide 33: Key Features
33
Extreme Visibility
  Peripheral Resolution by Stereo projection lens
  Super Dynamic 108dB
  Built in IR-LED supports 10m (only WV-X4571L)
  iA (intelligent Auto)
  Support Various dewarp mode (as same as current 9M 360 deg. Camera)
Extreme Compression
  H.265 + Smart Coding
Extreme Data Security
  Secure communication by Symantec certificate
  FIPS 140-2 Level 1 compliant
Extreme Analytics
  New People Counting * ASE303W
  People Counting, Heat-map and MOR * SAE200
Other Features
  IP66, IK10 support *WV-X4571L (Vandal Resistant Outdoor model)
  Anti-corrosion screw
  SD card error display
  Built in Dehumidifier
New 9M 360-deg. camera
WV-X4171/X4170
(Indoor)
WV-X4571L/X4171LM
(Outdoor Vandal with IR-LED)

## Slide 34: Easy Installation and Setting (WV-X4571L only)
Easy Kitting Packaging Kitting work without removing from the box Kitting time reduced by 3 minutes | RJ45 Joint Connector Waterproof tape processing unnecessary Installation time reduce by 3 minutes
Current condition
Rubber (2 pcs)
Taping for
waterproof
Extreme
Simplicity
X4571LM
X4571L
Installation time reduction by adopting “Easy Kitting Packing” and “RJ45 Joint Connector”

## Slide 35: Other Features: Angular Field of View Adjustment
X4171
X4571L
Easy Rotation Adjustment
New Attachment Bracket
Fixable in 3 position (-5, 0 and , +5 degree)
Double Panorama
Adjustable up and down, left and right
(Preset position setting)
Angular Field of View Adjustment
Single PTZ/Quad PTZ
Click & centering on live screen
Position selection on fish eye control screen
Fisheye
Adjustment is not required
* It is possible to attach the main body also to the conventional attachment metal fittings
Panorama
Adjustable up and down
(Preset position setting)
±5°
Newly applied “Rotation Adjustment” by changing rotation position of bracket
Extreme
Simplicity

## Slide 36: Key Features
36
Extreme Visibility
  Peripheral Resolution by Stereo projection lens
  Super Dynamic 108dB
  Built in IR-LED supports 10m (only WV-X4571L)
  iA (intelligent Auto)
  Support Various dewarp mode (as same as current 9M 360 deg. Camera)
Extreme Compression
  H.265 + Smart Coding
Extreme Data Security
  Secure communication by Symantec certificate
  FIPS 140-2 Level 1 compliant
Extreme Analytics
  New People Counting * ASE303W
  People Counting, Heat-map and MOR * SAE200
Other Features
  IP66, IK10 support *WV-X4571L (Vandal Resistant Outdoor model)
  Anti-corrosion screw
  SD card error display
  Built in Dehumidifier
New 9M 360-deg. camera
WV-X4171/X4170
(Indoor)
WV-X4571L/X4171LM
(Outdoor Vandal with IR-LED)

## Slide 37: Other Features (WV-X4571L only)
Impact resistance 50J/IK10 compatible
Vandal Roof *
Anti-corrosion screw *
Adoption of Anti-corrosion screws prevents sticking due to corrosion and improves maintainability
SD Card Error Display *
SD card error display LED
Installed in LED lighting unit seen from the outside
Dehumidifier *
Dehumidifying element mounted
37
* Support WV-X4571L only
X4571L
* Support WV-X4571L only
* Support WV-X4571L only
X4171
* Support WV-X4571L only
When a warning status is detected Lights red
  SD memory card warning detection conditions:
  After the total use time has exceeded 6 years and the number of overwrite times has exceeded 2000.
When an error status is detected Blinks red
  SD memory card error detection conditions: Write error, read error, etc.
Following Features of Conventional model and Extreme series

## Slide 38
i-VMD covering 360° wide area
Intruder detection
Detects people or cars trespassing in restricted areas.
Loitering detection
Detects people who has loitered for too long in the area.
Scene change detection
Detects tampering with the camera view.
Object detection (removed) Detects objects disappearing that should be present.
Cross line detection
Detects people or objects crossing the imaginary lines.
Object detection (left)
Detects something left behind that shouldn’t be there.
Other Features
X4171
X4571L
Intelligent Motion detection is supported
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 39
Business Intelligence in camera
Heat map
By overlaying the traffic volume of people and staying time, the 360 degree cameras visualize the movement of people in the area.
Moving Object Remover (MOR)
The 360 degree cameras enable customer behavior analysis, keeping their privacy. Moving Object Remover (MOR) makes moving objects translucent.
People count
By counting people who cross up to 12 imaginary lines in the 360° wide view, the 360-degree cameras help business improve the physical layout and operational efficiency.
Other Features
X4171
X4571L
Business intelligent function is supported
Notes: As first introduction of 4K cameras, we will launch 2 new 360 degree cameras;
One is WV-SFV481, outdoor vandal model, and the other is SFN480, indoor dome model.
The 3 major points are
ULTRA High Resolution 9M pixel as 360 degree camera
ULTRA High Sensitivity
ULTRA Intelligent

## Slide 40: Contents
Concept
Key features
      Extreme Visibility
      Extreme Compression
Image Capture mode
Supported Resolution
System Configuration
Specification Comparison
Bundled Items and Options
Model Number
Appearance
40
      Extreme Data Security
      Extreme Simplicity
      Other Features

## Slide 41: Restriction of Super Dynamic
41
When “On” is set for Super Dynamic, maximum frame rate becomes 15 fps because of the sensor capability.
GUI alert
1. Image Adjust window
2. Stream setup window
When “Set” is clicked on the specified condition, pop-up alert will be shown
"Frame rate" will become "15fps" at a maximum since "On" is set for "Super Dynamic".
X4170
X4571LM
X4171
X4571L
This message will be displayed to notice as restriction.

## Slide 42: Restriction of Super Dynamic
42
Manual (Operating Instruction)
(2.5.5.1 Configure the settings relating to image quality (“Image adjust” setup menu))
X4170
X4571LM
X4171
X4571L
Please make a note this restriction.

## Slide 43: GUI: Back Focus Setting
43
Focus area setting
When performing back focus, you can use this frame to specify the subject on the screen for which the focus should be adjusted. Unless specified otherwise, adjusts the focus to the subject in the central area of the screen.
Adjusting method (X4571L)
Auto/Preset / Fix
Auto: Adjusts the back focus function automatically and corrects the focus when switching between color
and black & white images.
Preset: Performs the preset movement to each specified back focus position when switching between color and black & white images.
Fix: Fixes the position after adjusting the back focus either automatically or manually
New
X4170
X4571LM
X4171
X4571L

## Slide 44: Image Capture Mode
44
[ Ceiling ] [ Wall ]
Fisheye
[ Ceiling ]
Double Panorama / Quad PTZ / Single PTZ / Fisheye + Double Panorama / Fisheye + Quad PTZ / Quad Stream
[ Wall ]
Panorama / Quad PTZ / Single PTZ / Fisheye + Panorama
Equivalent to WV-S4150
X4170
X4571LM
X4171
X4571L
Select image capture mode by setting position (Ceiling / Wall) and type
(Follow the specification of conventional camera)

## Slide 45: Image Capture Mode Comparison
Installation | WV-X4571L/X4171 New 9M 360-deg. | WV-S4550L/S4150 New 5M 360-deg. | WV-SFN480 Existing 9M 360-deg.
[ Ceiling ] [ Wall ] | Fisheye@30fps | Fisheye@30fps | 9M Fisheys@15fps 4M Fisheye@30fps
[Ceiling ] | Double Panorama / Quad PTZ / Single PTZ Fisheye + Double Panorama Fisheye + Quad PTZ / Quad Stream @15fps | Double Panorama / Quad PTZ / Single PTZ Fisheye + Double Panorama Fisheye + Quad PTZ / Quad Stream @30fps | Double Panorama@15fps Quad PTZ / Single PTZ@15fps 8M Fisheye + Double Panorama@7.5fps 4M Fisheye + Double Panorama@15fps 8M Fisheye + Quad PTZ@7.5fps 4M Fisheye + Quad PTZ@15fps Quad Stream@15fps
[ Wall ] | Panorama / Quad PTZ / Single PTZ Fisheye + Panorama @15fps | Panorama / Quad PTZ / Single PTZ Fisheye + Panorama @30fps | Panorama@15fps Quad PTZ / Single PTZ@15fps 8M Fisheye + Panorama@7.5fps 4M Fisheye + Panorama@15fps
45
*Stream(2) of Quad stream mode is 5fps (Same as 9M camera)
X4170
X4571LM
X4171
X4571L
Support 30fps output in Fisheye, 15fps output in High Resolution De-warp mode.

## Slide 46: Max. Resolution Comparison
 | Image | WV-X4571L/X4171 New 9M 360-deg. |  | WV-S4550L/S4150 New 5M 360-deg. |  | WV-SFN480 (9M) Existing 9M 360-deg. |  | Remarks
 |  | JPEG | H.265/264 | JPEG | H.265/264 | JPEG | H.264 | 
1 | Fisheye | 2992x2992 | 2992x2992 | 2192x2192 | 2192x2192 | 2992x2992 | 2992x2992 | 
2 | Double Panorama Panorama | 2560x1440 | 2560x1440 | 1920x1080 | 1920x1080 | 2560x1440 | 2560x1440 | 
3 | Quad PTZ Single PTZ | 2560x1920 | 2560x1920 | 1600x1200 | 1600x1200 | 2560x1920 | 2560x1920 | 
46
X4170
X4571LM
X4171
X4571L
The Max. output resolution is equivalent to the existing model

## Slide 47: Supported Resolution (1/2)
 | Capture Image Mode | Stream (1) (H.265/ H.264) | Stream (2) (H.265/ H.264) | JPEG (1) | JPEG (2) | Max. fps
1 | Fisheye (Ceiling / Wall) | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Fisheye 1280x1280 640x640 320x320 | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Fisheye 1280x1280 640x640 320x320 | Stream:30fps JPEG: 5fps when using stream, and 15fps when not using stream.
2 | Double Panorama (Ceiling) | ■Double Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | ■Double Panorama 1920x1080 1280x720 640x360 320x180 | ■Double Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | ■Double Panorama 1920x1080 1280x720 640x360 320x180 | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
3 | Panorama (Wall) | ■Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | ■Panorama 1920x1080 1280x720 640x360 320x180 | ■Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | ■Panorama 1920x1080 1280x720 640x360 320x180 | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
4 | Quad PTZ (Ceiling / Wall) | ■Quad PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA QVGA | ■Quad PTZ 1280x960 800x600 VGA QVGA | ■Quad PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA QVGA | ■Quad PTZ 1280x960 800x600 VGA QVGA | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
47
X4170
X4571LM
X4171
X4571L

## Slide 48: Supported Resolution (2/2)
 | Capture Image Mode | Stream (1) (H.265/ H.264) | Stream (2) (H.265/ H.264) | JPEG (1) | JPEG (2) | Max. fps
5 | Single PTZ (Ceiling / Wall) | ■Single PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA, QVGA | ■Single PTZ 1280x960 800x600 VGA QVGA | ■Single PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA, QVGA | ■Single PTZ 1280x960 800x600 VGA QVGA | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
6 | Fisheye + Double Panorama (Ceiling) | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640, 320x320 | ■Double Panorama 1280x720 640x360 320x180 | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Double Panorama 1280x720 640x360 320x180 | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
7 | Fisheye + Panorama (Wall) | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Panorama 1280x720 640x360 320x180 | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Panorama 1280x720 640x360 320x180 | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
8 | Fisheye + Quad PTZ (Ceiling / Wall) | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Quad PTZ 1280x960 800x600 VGA QVGA | ■Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | ■Quad PTZ 1280x960 800x600 VGA QVGA | Stream:15fps JPEG: 5fps when using stream, and 15fps when not using stream.
9 | Quad Stream (Ceiling) | ■Single PTZ (Ch1-Ch4) 1280x960 800x600 VGA QVGA | ■Quad PTZ 2560x1920 2048x1536 1600x1200 1280x960, 800x600, VGA, QVGA |  |  | Stream (1) ⇒ 15fps -------------- Stream (2) ⇒ 5fps
48
X4170
X4571LM
X4171
X4571L

## Slide 49: Bitrate Table (H.265)
49
* This table is valid only for group-10.
Unit: kbps
* Please access to SSBD wiki for more details data.
http://10.75.24.156/en/index.php/h.265bitrate
X4170
X4571LM
X4171
X4571L
Resolution | Image Quality | Frame Rate [fps] |  |  |  |  |  |  |  | 
 |  | 1 | 3 | 5 | 7.5 | 10 | 12 | 15 | 20 | 30
640x640 | XF | 384 | 512 | 512 | 512 | 512 | 640 | 640 | 768 | 768
 | SF | 256 | 384 | 384 | 384 | 384 | 448 | 448 | 640 | 640
 | FQ | 224 | 320 | 320 | 320 | 320 | 352 | 352 | 448 | 448
 | NQ | 128 | 256 | 256 | 256 | 256 | 256 | 256 | 384 | 384
1280x1280 | XF | 1280 | 1536 | 1536 | 1536 | 1536 | 1536 | 1536 | 2048 | 2048
 | SF | 768 | 1280 | 1280 | 1280 | 1280 | 1280 | 1280 | 1536 | 1536
 | FQ | 512 | 768 | 768 | 768 | 768 | 896 | 896 | 1024 | 1024
 | NQ | 384 | 512 | 512 | 512 | 512 | 768 | 768 | 768 | 768
2192x2192 | XF | 2048 | 3072 | 3072 | 3072 | 4096 | 4096 | 4096 | 6144 | 6144
 | SF | 1536 | 2048 | 2048 | 2560 | 3072 | 3072 | 3072 | 4096 | 4096
 | FQ | 1280 | 1536 | 1536 | 1792 | 2560 | 2560 | 2560 | 3072 | 3072
 | NQ | 1024 | 1280 | 1280 | 1536 | 1792 | 1792 | 1792 | 2560 | 2560
2992x2992 | XF | 4096 | 6144 | 6144 | 6144 | 7168 | 7168 | 8192 | 10240 | 10240
 | SF | 3072 | 4096 | 4096 | 5120 | 6144 | 6144 | 6144 | 8192 | 8192
 | FQ | 2560 | 3072 | 3072 | 3584 | 3584 | 3584 | 5120 | 6144 | 6144
 | NQ | 1792 | 2048 | 2048 | 2048 | 2560 | 2560 | 2560 | 3584 | 3584

## Slide 50: System Configuration
50
[ Pattern 1 ]
Simultaneous delivery of high resolution fisheye images for recording and low resolution Fisheye for live
L3 Switch
ASM300 / VMS
Monitors
For Recording: Stream(1), 9M Fisheye, 30fps
Record
Quad PTZ / Panorama
Double Panorama
For Live: Stream(2), VGA Fisheye, 30fps
VMS or NX series recorder
Live
Compensation
Playback
Single PTZ / Quad PTZ
Panorama / Double Panorama
Confirm any place afterward
Arbitrarily select display pattern
Compensation
X4170
X4571LM
X4171
X4571L
Assume the same system configuration conventional 9M camera except for frame rate

## Slide 51: System Configuration
51
[ Pattern 2 ]
Simultaneous delivery of high resolution fisheye images for recording and low resolution Quad PTZ for live
L3 Switch
ASM300 / VMS
Monitors
For Recording: Stream(1), 9M Fisheye, 30fps
Record
Quad PTZ
For Live: Stream(2), Quad PTZ, 15fps
Live
Playback
Operation is similar with 4 fixed cameras
VMS or NX series recorder
Confirm any place afterward
Single PTZ / Quad PTZ
Panorama / Double Panorama
Compensation
X4170
X4571LM
X4171
X4571L
Assume the same system configuration conventional 9M camera except for frame rate
Framerate will be 15fps in case of Quad PTZ for live.
* 5M camera (WV-S4150/S4550L) will be 30fps.

## Slide 52: Spec. Comparison (Indoor Model) 1/2
Model No. | Existing 9M 360-deg. WV-SFN480 | New 9M 360-deg. WV-X4171 | New 9M 360-deg. WV-X4170 | 5M 360-deg. WV-S4150
Appearance |  |  |  | 
Image Sensor | 1/2" 9MP CMOS | 1/2" 9MP CMOS | 1/2" 9MP CMOS | 1/3" CMOS
Lens(focal length, F) | 1.4 / F1.9 | 1.4 / F1.9 | 1.4 / F1.9 | 0.84mm / F2.4
Minimum Illumination | 0.3 lx | 0.3 lx | 0.3 lx | 0.3 lx
Intelligent Auto | N/A | Yes | Yes | Yes
Super Dynamic, Dynamic Range | N/A, 84dB | YES, 108dB | YES, 108dB | YES, 108dB
Wide Dynamic Range | YES | YES (Next version up) | YES (Next version up) | N/A
IR-LED, irradiation distance | N/A | N/A | N/A | N/A
Angular Field of view | H 180°/V 180° | H 183°/V 183° | H 183°/V 183° | H/V 186°
Video Compression | H.264/ MJPEG | H.265/ H.264/ MJPEG | H.265/ H.264/ MJPEG | H.265/ H.264/ MJPEG
Image Resolution(max)/ Frame Rate(max) | 2992x2992 / 15fps | 2992x2992 / 30fps * Super Dynamic “On”: Max. 15fps | 2992x2992 / 30fps * Super Dynamic “On”: Max. 15fps | 2192x2192 / 30fps
Smart Coding | Yes | Yes | Yes | Yes
Audio Compression | G.726, G.711, AAC-LC | G.726, G.711, AAC-LC | N/A | G.726, G.711, AAC-LC
Security standard | N/A | FIPS140-2 Level1 | FIPS140-2 Level1 | FIPS140-2 Level1
52
Improvements from the existing model: iA, Super Dynamic, H.265, Framerate and Secure
X4170
X4171

## Slide 53: Spec. Comparison (Indoor Model) 2/2
Model No. | Existing 9M N/A360-deg. WV-SFN480 | New 9M 360-deg. WV-X4171 | New 9M 360-deg. WV-X4170 | 5M 360-deg. WV-S4150
Appearance |  |  |  | 
Power Source | DC12V, PoE(class0) | DC12V, PoE(class0) | DC12V, PoE(class0) | DC12V, PoE(class2)
Ambient Operating Temperature | -10～+50℃ | -10～+50℃ | 0～+40℃ | -10～+50℃
External I/O Terminals | 3 | 3 | N/A | 3
Built in Mic | Yes | Yes | N/A | Yes
Mic (Line) Input | Yes | Yes | N/A | Yes
Audio Output | Yes | Yes | N/A | Yes
Water and Dust Resistance | N/A | N/A | N/A | N/A
Shock Resistance | N/A | N/A | N/A | N/A
Dimensions | φ150 x 52.1mm | φ150 x 49.5mm | φ150 x 49.5mm | φ150 x 50.5mm
Mass (approx.) | 480g | 420g | 420g | 390g
VMD, People count, etc. | Yes | Yes | Yes | Yes
New People count | N/A | Yes | N/A | Yes
Tripod screw | Yes | Yes | N/A | Yes
53
X4170
X4171

## Slide 54: Spec. Comparison (Outdoor Model) 1/2
Model No. | Existing 9M 360-deg. WV-SFV481 | New 9M 360-deg. WV-X4571L/X4571LM | 5M 360-deg. WV-S4550L
Appearance |  |  | 
Image Sensor | 1/2" 9MP CMOS | 1/2" 9MP CMOS | 1/3" CMOS
Lens(focal length, F) | 1.4 / F1.9 | 1.4 / F1.9 | 0.84 / F2.4
Minimum Illumination | 0.3 lx | 0.3 lx | 0.3 lx
Intelligent Auto | N/A | Yes | Yes
Super Dynamic, Dynamic Range | N/A, 84dB | Yes, 108dB | Yes, 108dB
Wide Dynamic Range | YES | YES (Next version up) | N/A
IR-LED, irradiation distance | N/A | Yes, 10m (When Intensity control is “ON”) | Yes, 10m (When Intensity control is “ON”)
Angular Field of view | H 180°/V 180° | H 183°/V 183° | H/V 186°
Video Compression | H.264/ MJPEG | H.265/ H.264/ MJPEG | H.265/ H.264/ MJPEG
Image Resolution(max)/ Frame Rate(max) | 2992x2992 / 15fps | 2992x2992 / 30fps * Super Dynamic “On”: Max. 15fps | 2192x2192 / 30fps
Smart Coding | Yes | Yes | Yes
Audio Compression | G.726, G.711, AAC-LC | G.726, G.711, AAC-LC | G.726, G.711, AAC-LC
Security standard | N/A | FIPS140-2 Level1 | FIPS140-2 Level1
54
Improvements from the existing model: iA, IR-LED, Super Dynamic, H.265, Framerate and Secure
X4571LM
X4571L

## Slide 55: Spec. Comparison (Outdoor Model) 2/2
Model No. | Existing 9M 360-deg. WV-SFV481 | New 9M 360-deg. WV-X4571L/X4571LM | 5M 360-deg. WV-S4550L
Appearance |  |  | 
Power Source | DC12V, PoE(class0) | DC12V, PoE(class0) | DC12V, PoE(class0)
Ambient Operating Temperature | -40～+50℃ | -40～+60℃ | -40～+60℃
External I/O Terminals | 3 | 3 | 3
Built in Mic | N/A | N/A | N/A
Mic (Line) Input | Yes | Yes | Yes
Audio Output | Yes | Yes | Yes
Water and Dust Resistance | IP66 | IP66 | IP66
Shock Resistance | 50J, IK10 | 50J, IK10 | 50J, IK10
Dimensions | φ164 x 96.5mm (When using Base Bracket) | φ164 x 96.3mm (When using Base Bracket) | φ164 x 96.3mm (When using Base Bracket)
Mass (approx.) | 1.3kg (When using Base Bracket) | 1.3kg (When using Base Bracket) | 1.3kg (When using Base Bracket)
55
Improvements from the existing model: Ambient Operating Temperature
X4571LM
X4571L

## Slide 56: Other function list
56
No | Function |  | 9MP SFN480 | Fixed Dome S2131L | 5MP S4150 | New 9MP X4571 | Note
1 | Video transmittance | Smart Coding (GOP control) | Yes Off/Low/Mid/ High | Yes Off/Low/Mid/ Advanced | Yes Off/Low/Mid/ Advanced/ Frame rate control | Yes Off/Low/Mid/ Advanced/ Frame rate control | 
2 |  | Smart Coding (Auto VIQS) | Yes | Yes | Yes | Yes | 
3 |  | Face Smart Coding | N/A | Yes | N/A | N/A | 
4 |  | Number of video stream | 2 | 4 | 2 | 2 | 
5 |  | Stream priority | Yes | N/A | N/A | N/A | 
6 |  | VIQS (Fixed area setting) | Yes (8 area) | N/A | Yes (8 area) | Yes (8 area) | 
7 |  | Decode (ActiveX) | Software (Fixed) | Software (Fixed) | Hardware /Software *selectable | Hardware /Software *selectable | When selecting hardware, Intel Core i5-6500, Intel Core i7-6700 is required for PC spec.
8 |  | Stream Shaping | N/A | Yes Default: Off | Yes Default: On | Yes Default: On | Countermeasure for packet loss by burst
9 |  | Number of simultaneous access users | 14 | 14 | 14 | 14 | 
X4170
X4571LM
X4171
X4571L
Notes: 288kmph= カトリーナ：280 km/h
伊勢湾台風=270km/h

## Slide 57: Other function list
57
No | Function |  | 9MP SFN480 | Fixed Dome S2131L | New 5MP S4150 | New 9MP X4571 | Note
10 | Analytics | Motion detection (VMD) | Yes | Yes | Yes | Yes | 
11 |  | Video Analytics (i-VMD) | Yes | Yes | Yes | Yes | SAE200
12 |  | Video Analytics (Heat map, people count, MOR) | Yes | N/A | Yes | Yes | SAE200
13 |  | New people count | N/A *Project base | N/A | Yes | Yes | SAE303W Not support for MP version. Will be updated by firmware version up
14 |  | Face detection | N/A | Yes | N/A | N/A | 
15 | SD recording | The number of recording stream | 1stream | 2stream | 1stream | 1stream | 
 |  | Password lock | N/A | N/A -> Yes | N/A | Yes | Will be updated by firmware version up
16 |  |  |  |  |  |  | 
17 | Rotation adjustment (Fisheye) |  | +/- 45 deg. by mechanical | N/A | -5, 0, +5 deg. by attachment plate | -5, 0, +5 deg. by attachment plate | 
18 | Rotation adjustment (Panorama) |  | +/- 45 deg. by mechanical and 90 deg. by software | N/A | -5, 0, +5 deg. by attachment plate | -5, 0, +5 deg. by attachment plate | 
19 | Rotation adjustment (Double Panorama) |  | +/- 45 deg. by mechanical and 90 deg. by software | N/A | as above + by software | as above + by software | 
X4170
X4571LM
X4171
X4571L
Notes: 288kmph= カトリーナ：280 km/h
伊勢湾台風=270km/h

## Slide 58: Bundled Items
58
  ■ WV-S4571L
No. | Item | Q’ty
1 | Installation Guide | 1 set
2 | Important Safety Instructions | 1 pc.
3 | Warranty card *1 | 1 set
4 | CD-ROM *2 | 1 pc.
5 | Code label *3 | 1 pc
6 | Base Bracket | 1 pc
7 | Attachment Plate | 1 pc
8 | Fixing screws for attachment plate | 5 pc
9 | Template A (for the attachment Plate) | 1 pc.
10 | Template B (for base bracket) | 1 pc
11 | Waterproof tape | 1 pc
12 | 4P alarm Cable | 1 pc
13 | 2P power Cable | 1 pc
14 | Bit (Hex wrench, screwsize6.35mm{1/4inches}T20 | 1 pc
15 | RJ45 Waterproof connecter cover | 1 pc
16 | RJ45 Waterproof connecter cap | 1 pc
*1 This product comes with several types of warranties. Each warranty is only applicable to the products purchased in the regions indicated on the relevant warranty.
*2 The CD-ROM contains the operating instructions and different kinds of tool software programs.
*3 This label may be required for network management. Use caution not to lose this label.
*4 The power cord plug is attached to the camera.
*5 The screws are necessary when installing the camera on a separately sold mount bracket.
  ■ WV-X4171
No. | Item | Q’ty
1 | Installation Guide | 1 pc.
2 | Important Safety Instructions | 1 pc.
3 | Warranty card | 1 pc.
4 | CD-ROM *2 | 1 pc.
5 | Code label *3 | 1 pc.
6 | Attachment Plate | 1 pc.
7 | Audio Cable*4 | 1 set
8 | Power cord plug*4 | 1 pc.
9 | External I/O terminal plug | 1 pc.
10 | Template A(for Attachment Plate) | 1 pc.
11 | Cable tie | 2 pc.
12 | Safety wire lug | 1 pc.
13 | Safety wire | 1 pc.
14 | Washer | 1 pc.
15 | Spring washer | 1 set
X4170
X4571LM
X4171
X4571L

## Slide 59: Options
  ■ Mount Bracket and Attachment Pipe
59
1. WV-Q121B (Silver)
Ceiling Mount Bracket
WV-X4170/X4171
WV-X4571L
3. WV-Q124 (Silver)
Mount Bracket
6. WV-Q123
Pipe Mount Bracket
(For Japan only)
2. WV-Q180
Indoor Mount Bracket
(For X4171 only) (For Japan only)
2. WV-Q122A (Silver)
Wall Mount Bracket
1. WV-Q105A
Ceiling Mount Bracket
4. WV-Q185 (Light gray)
Wall Mount Bracket
5. WV-Q186 (Light gray)
Mount Bracket
X4170
X4571LM
X4171
X4571L

## Slide 60: Model Number
60
W | V |  | X | 4 | 1 | 7 | 1/0 |  |  |  | 
W | V | - | X | 4 | 5 | 7 | 1 | L | M |  | 
 |  |  | Series | Form | Environment | Resolution | Serial number | Other features |  | Minor Change | Region (J/H)
 |  |  | X:X series High - end S:S series High specification & High cost performance V:V series Price competiveness | 9：- 8：Multi sensor 7：PTZ(Aero) 6：PTZ(Dome) 5：PT 4：360 deg. 3：Compact DOME 2：Dome 1：Box 0 : - | 9：- 8：- 7：- 6：- 5：Outdoor Vandal 4：Outdoor normal 3：- 2：Indoor Vandal 1：Indoor normal 0：- | 9：- 8 :6K(24MP) 7 :4K (12MP) 6 : 5 :5MP 4： 3 :FHD 2 : 1 :HD 0 :- | 9 : 8 : 7 : 6 : 5 : 4 : 3 : 2 : 1 : 0： | L : LED N: Rain wash coating (Non Raindrop) M: M12 W: Wireless F : Optical I/F V : With lens T : Long focal lens K : Fix lens |  | D : C : B : A : | 
3rdgen.
2nd gen.
1st gen.
Reserve
Model Name | Model Number
9M 360-deg. Indoor Camera | WV-X4171/X4170
9M 360-deg. Outdoor Camera | WV-X4571L/X4571LM
X4170
X4571LM
X4171
X4571L

## Slide 61: Appearance (WV-X4171/X4170)
61
Dimensions: Φ150 x 49.5 mm (H)
Weight: Approx.420g
X4170
X4171

## Slide 62: Appearance (WV-X4571L/X4571LM)
62
Dimensions: Φ164 x 96.3 mm (H)
Weight: Approx.1.3 kg with Base
Approx.880g with Attachment
X4571LM
X4571L

## Slide 63: PC specification for 9M 360 deg. camera
63
Since 9M pixel is high resolution, High performance PC also be required for display.
Necessary PC specification (It is same specification with ASM300 rest of Graphic accelerator)
  Follow specification as below.
  Use smooth buffering mode on camera browser.
  Use Hardware decode function on camera browser.
    For H.265 Hardware decoding, at least one monitor should be connected to onboard Graphics as a main display.
  Use display port Ver.1.2.
System requirements | 
CPU | Intel® Core™ i7-6700 or faster
Memory | - 8GB or more - Using the dual channel corresponding memory, it is the memory of the same performance and requires the use of in pairs. (e.g.：In the case of 8GB, use 2pcs of 4GB memory)
Graphic accelerator | - VRAM: 512MB or more, compatible with Microsoft® DirectX® 9.0c or later - Using 4K display, it requires NVIDIA Quadro P600 especially for 9M pixel 30fps monitoring. Without the Graphics board, it is necessary to use FHD display or 9M 15fps setting.
OS | Microsoft® Windows® 10 64bit
X4170
X4571LM
X4171
X4571L

## Slide 64: GUI: Easy Setup
Easy Setup
The “Easy Setup” page uses simple operations to set the following:
Internet setup:
  Make the camera image available on the Internet
Event action setup:
  Set event actions such as recording of a schedule/alarm to the SD memory card
64
Internet
Event action
X4170
X4571LM
X4171
X4571L

## Slide 65: GUI: Decoding option / Audio out
■Decoding option
Software / Hardware
Software: Decoded by software.
Hardware: Decoded by using hardware acceleration (QSV / DXVA) function with high speed.
Confirm button
Possible to confirm whether the using PC can support Hardware decoding. (Following three judgement)
Possible to use Hardware decoding for both H.265 and H.264.
Possible to use Hardware decoding for H.264 only.
Impossible to use Hardware decoding
Audio out
Audio / Monitor
Audio: Use as Audio output
Monitor: Use as monitor output
New!!
New!!
Change!!
65
Basic (Basic menu)
Note: When the bit rate is higher than 2192x2192, 30fps, 8Mbps, please use Hardware decoding. (Recommended PC specification: Intel Core i7-6700 or faster processor, OS type: In case of H.265: Use Windows 10, In case of H.264: Use Windows 7 or later)
Note: If the PC is not suitable for Hardware decoding, the following message will be displayed.
Note: Can be used monitor output regardless image capture mode.
(WV-SFV481/SFN480 is available monitor output when selecting Fisheye mode only.)
X4170
X4571LM
X4171
X4571L

## Slide 66: GUI: SD memory card (X4571L/X4571LM only)
SD memory card warning / error LED
Off / On
On: When a warning status is detected, the SD memory card error/error LED turns on. When an error status is detected, the SD memory card error/error LED starts flashing.
Off: Stops detection of warning or error status.
66
SD memory card warning / error LED
Note:
SD memory card warning detection conditions: After the total use time has exceeded 6 years and the number of overwrite times has exceeded 2000.
When recognition error and warning occur at the same time, recognition error display (blinking) is made.
Flashing cycle is 500 msec. on, 500 msec. off
Caution:
When using "SD memory card warning / error lamp" ON, the SD memory card warning / error lamp may appear in the image in the surrounding environment etc.
Select On/Off to determine whether or not to activate the SD memory card warning/error LED when an SD memory card warning or error is detected.
X4571LM
X4571L

## Slide 67: GUI: Image Adjust (Basic menu)
Basic Menu
Dynamic range
Off/ On(Super Dynamic)
Light control mode
ELC/ Indoor scene(50Hz) / Indoor scene(60Hz)
Day & Night (electrical) (S4150,X4171 only)
Off/ Auto
Day & Night (S4550L,X4571L only)
Off/ On(IR Light Off)/ On(IR Light On)/ Auto1(IR Light Off)/
Auto2(IR Light On)/ Auto3(SCC)
White balance: ATW1/ ATW2/ AWC
Intelligent auto: On/ Off
Detailed setting
Scene registration
67
Change!!
X4170
X4571LM
X4171
X4571L

## Slide 68: GUI: Image Adjust (Super Dynamic)
Dynamic range
Off/ On(SuperDynamic) / On(Wide dynamic range)
Level: 0 to 31 Super Dynamic level setting (Default: 28)
BLC / HLC
Off/ Back light compensation(BLC) / High light compensation(HLC)
*Default is Off: Deactivates the back light compensation function and high light compensation function.
Note: When “On” is selected for “Super Dynamic(SD)” or when “On” is selected for “Intelligent Auto”, this setting is not available.
BLC level: 0 to 31 level setting (Default: 16)
HLC level: 0 to 31 level setting (Default: 16)
Mask area
12x12
Note: When “On” is selected for “Super Dynamic(SD)”, this setting is not available.
Regardless of the “Image capture mode” setting, Fisheye images are configured for mask settings.
IMPORTANT: The mask area may move out of alignment if the setting for “Image capture mode” of the [Image] tab
or “Upside-down” of the [Basic] tab is changed after the mask area has been configured. Make sure to check the mask area after changing the “Image capture mode” setting.
Change!!
12
Dynamic range
68
Can be set more finely than previous 9M 360-deg camera (WV-SFN480) (8x8)
12
On(スーパーダイナミック)設定時は、フレームレートが最大15fpsに
制限されます
Change!!
X4170
X4571LM
X4171
X4571L

## Slide 69: GUI: Image Adjust (Light control mode)
Light control mode
ELC/ Indoor scene(50Hz) / Indoor scene(60Hz)
*The shutter speed will automatically be adjusted to prevent flicker caused by fluorescent light. Select 50 Hz or 60 Hz corresponding to the location where the camera is in use.
Brightness: 0 to 255 (Default: 64)
Maximum gain: 0 to 11 (Default: 9)
* When the luminance of the subject becomes darker, gain will be automatically increased and screen will become brighter. If you increase the gain, the noise may also increase.
Maximum shutter
Max.1/10000s, Max.1/4000s, Max.1/2000s, Max.1/1000s, Max.1/500s, Max.1/250s, Max.1/120s, Max.1/100s, Max.2/120s, Max.2/100s, Max.3/120s, Max.1/30s, Max.2/30s, Max.4/30s, Max.6/30s, Max.10/30s, Max.16/30s
(There are total 17 patterns available, Default: Max 1/30s)
Light control speed: 0 ～ 31 (Default: 16)
69
Light control mode
X4170
X4571LM
X4171
X4571L

## Slide 70: GUI: Image Adjust (Day & Night)
Day & Night (S4550L)
Off/ On(IR Light Off)/ On(IR Light On)/ Auto1(IR Light Off)/ Auto2(IR Light On)/ Auto3(SCC)
*Default is Auto2(IR Light On): The camera automatically switches between the color mode and the black & white mode in accordance with the picture brightness (luminance). Suitable when using near-infrared lighting at night.
Level: High/ Low
Dwell time: 2s/ 10s/ 30s/ 1min
IR LED light intensity: High/ Middle / Low
Intensity control: On / Off
Change!!
70
Day & Night
X4171/4170 GUI
X4571L/X4571LM GUI
Day & Night (electrical) (S4150)
Off/ Auto
Off: The color mode is selected.
Auto: Switches from color to black-and-white images when the ambient brightness (illuminance) of the camera is approx. 1.0 lx or less. It takes time to switch between modes.
X4170
X4571LM
X4171
X4571L

## Slide 71: GUI: Image Adjust (White balance)
White balance
ATW1/ ATW2/ AWC
Note:
Under the following conditions, color may not be faithfully processed. In these cases, select “AWC”.
  - When shooting a subject whose major part is a thick color
  - When shooting blue sky or sun at sunset
  - When shooting a subject whose luminance is too low
When “AWC” is selected, click the [Set] button.
Red gain
0 to 255 level setting (Default: 128)
Blue gain
0 to 255 level setting (Default: 128)
Mask area
12x12
Adjustment speed
0 to 31 level setting (Default: 16)
Change!!
71
White balance
X4170
X4571LM
X4171
X4571L
Can be set more finely than previous 9M 360-deg camera (WV-SFN480) (8x8)

## Slide 72: GUI: Image Adjust (Intelligent auto / Scene registration)
Intelligent auto
On/ Off
Motion priority level
0 to 255 level setting (Default: 128)
Scene file
1: Scene 1, 2: Scene 2, 3: Scene 3, 4: Scene 4 (up to 4 files can be registered)
Scene file title
The scene file name (up to 10 characters) displayed in “Scene file” can be changed. Only file names displayed in “1:”, “2:”, “3:”, and “4:” can be changed.
* Unavailable characters: " &
[Load] button: Loads the setting data selected in “Scene file” and changes the current image accordingly.
[Register] button: The combination of settings used to adjust image quality that are currently displayed can be registered to the scene file displayed in “Scene file”.
Change!!
72
Intelligent auto
Scene registration
Note: “Face priority” is not applied 5MP 360-deg. camera
“Intelligent Auto” can detect conditions (back lighting, outdoor, night time, etc.) or moving objects and then automatically adjust the camera’s aperture, gain, shutter speed, and contrast in order to display moving objects more clearly.
X4170
X4571LM
X4171
X4571L

## Slide 73: GUI: Image Adjust (Detailed setting)
Auto contrast adjust
On/ Off(Manual)
Contrast level
0 to 255 level setting (Default: 128)
Adaptive black stretch
0 to 255 level setting (Default: 128)
Adaptive highlight stretch
0 to 255 level setting (Default: 128)
Fog compensation
On/ Off
Level
0 to 127 level setting
New
73
Detailed setting
Chroma gain level
0 to 255 level setting (Default: 128)
Hue level
0 to 255 level setting (Default: 128)
Aperture level
0 to 31 level setting (Default: 16)
Pedestal level
0 to 255 level setting (Default: 128)
DNR
0 to 255 level setting (Default: 128)
The following three functions have been newly added to WV-S4150/4550L, which 9M 360-deg camera does not support.
Auto contrast adjust: Select On/Off(Manual) to determine whether or not to activate the auto contrast adjust function.
Adaptive highlight stretch: Adjust the brightness of the bright parts of the image.
Fog compensation: The fog compensation function can make dim images that have been affected by fog or other conditions clearer using digital image processing.
Note: When “On” is selected for “Auto contrast adjust”, or when “On” is selected for “Intelligent Auto”, this setting is not available.
New
New
X4170
X4571LM
X4171
X4571L

## Slide 74: GUI: Encoding format / Transmission priority
Stream encoding format
H.265 / H.264
* The stream encoding format can be selected for stream 1 and 2 respectively, such as Stream 1 as H.265, stream 2 as H.264.
Transmission priority
Frame rate / Constant bit rate / VBR / Best effort
Note:
Default setting of the Transmission priority has been changed to unified in the same as other Extreme series cameras.
When “Frame rate” is set for “Transmission priority”, number of users who can access the camera may be limited.
Change!!
74
Image tab on Image/Audio menu
X4170
X4571LM
X4171
X4571L

## Slide 75: GUI: Smart coding (GOP control / Auto VIQS)
GOP control
Can be reduced data amount in areas where there is no motion. Available mode is different depends on encoding format.
A) In case of H.265 is selected
Off / On(Low) / On(Mid)/ On(Advanced)/ On(Frame rate control)
B) In case of H.264 is selected
Off / On(Low) / On(Mid)
Off:
On(Low): I frame interval: 1 to 8 sec.
On(Mid): I frame interval: 4 to 16 sec.
On(Advanced): I frame interval: 60 sec.
On(Frame rate control):
  By dynamically controlling the frame rate in addition to the refresh interval depending on the presence or absence of motion, the bit rate at the time of scene shooting without motion is further reduced.
Auto VIQS
Keeps high image quality in the motion area and suppresses the amount of data in other areas.
Off /On
New!!
75
Image tab on Image/Audio menu
New!!
X4170
X4571LM
X4171
X4571L

## Slide 76: GUI: Audio
Audio input
Mic select (S4150 only)
Mic input volume
AGC (audio)
Audio bit rate
* Common use for both recording and transmission
Audio transmission
Setup relating audio transmission
Audio transmission mode
Mic input interval (Camera to PC)
Audio output volume (PC to Camera)
Audio output interval (PC to Camera)
Audio output duration
Audio output port (PC to Camera)
Audio input encoding format
76
Audio input / Audio transmission
X4170
X4571LM
X4171
X4571L

## Slide 77: GUI: Alarm
It is possible to select which alarm to notify by e-mail for each e-mail notification destination.
For alarm FTP and alarm recording, it is also possible to select which alarm to operate
77
Alarm E-mail notification
Alarm image FTP transmission
Alarm image recording(SD memory card)
Select functions to be activated by cause of alarm:
E-mail notification (per destination) / FTP transmission / SD recording
X4170
X4571LM
X4171
X4571L

## Slide 78: GUI: Alarm E-mail notification
E-mail subject
There are two options
Use the camera title
Cause of alarm
Discrimination of sender and cause of alarm discrimination can be done only by mail title.
E-mail body
There are two options
Cause of alarm
Occurrence time
Terminal name
Describe terminal name when the alarm is occurred.
78
E-mail subject / E-mail body / Terminal name
X4170
X4571LM
X4171
X4571L

## Slide 79: GUI: User auth.
User name registration
“--New registration--” will be displayed when clicking pulldown menu
When clicking pulldown menu, registered user name will be displayed
Up to 23 users can be registered
Access level
Possible to change from the pulldown menu.
There are three options are selectable.
1. Administrator
2. Camera control
3. Live only
79
User name registration / Access level
Note:
When "- new registration -" is selected, "change" and "delete" are grayed out.
When "Registered" user name is selected, "Change" and "Delete" become effective.
When “- new registration –”” is selected, register as new user name.
When “Change” is selected, Information on the selected user name is displayed in "User name" "Access level". The rest is the same as new registration.
When “Delete” is selected, the selected user is deleted..
X4170
X4571LM
X4171
X4571L

## Slide 80: GUI: Data encryption
Data encryption (Batch change)
On / Off
On : Encrypt data and distribute it
The password is required to open Live stream and
setting screen which is including video distribution.
Off : No data encryption
Change!!
80
Data encryption (User mng. menu)
Note:
It can not be used when the imaging mode is Quad stream.
Only AAC-LC is encrypted for Audio.
When encryption is set, the recording data is also encrypted.
Previous 9M 360-deg camera (WV-SFN480) does not have this function.
X4170
X4571LM
X4171
X4571L

## Slide 81: GUI: Schedule
Schedule mode
There are total 14 patterns are available
Off
Alarm permission (Terminal alarm 1, 2, 3)
Alarm permission (Terminal 1)
Alarm permission (Terminal 2)
Alarm permission (Terminal 3)
VMD permission
Access permission
H.264 recording
Image adjust 1: Scene 1
Image adjust 2: Scene 2
Image adjust 3: Scene 3
Image adjust 4: Scene 4
FTP periodic image transmission
E-mail permission
81
Schedule mode
Note
When “Quad stream” is selected for “Image capture mode”, “FTP periodic image transmission”
cannot be selected.
X4170
X4571LM
X4171
X4571L

## Slide 82: Thank you